Fact Sheet

Carriage of Dangerous Goods

Ventilation Requirements

EU rules for the carriage of dangerous goods by road are contained in the ADR international accord documents.

These are then incorporated into British law by the "Carriage of Dangerous Goods and Use of Transportable Pressure Equipment Regulations 2007" ("CDG").

Specific rules concerning the ventilation of dangerous goods during transportation are found in ADR Section 7.5.11 (and CDG regulation 62 6a) under Code CV36 which states that:

"CV36 Packages shall preferably be loaded in open or ventilated vehicles or open or ventilated containers.

If this is not feasible and packages are carried in closed vehicles or containers, the cargo doors of the vehicles or containers shall be marked with the following in letters not less than 25MM high: WARNING NO VENTILATION OPEN WITH CARE. This shall be in a language considered appropriate by the consignor."

The rules apply to all sizes of vehicles and in theory to any quantity of dangerous goods.

The rules must be applied to vehicles where it is "feasible" to install ventilation.

The use of warning signs is only permitted as an alternative to ventilation where vehicles are exceptionally or only very occasionally used for CV36 code goods or if there is some peculiar vehicle design feature, or if the proportion of the load with this code is very small.

Code CV36 applies to goods that have the following UN numbers:

UN 1001-1078, 1581/2, 1612,1749, 1858-60, 1911-3, 1951-84, 2034-6, 2044, 2187-2204, 2417-24, 2451-4, 2534, 2548, 2591-2602, 2676, 3057, 3070, 3083, 3153-3163, 3220, 3252, 3296-3300, 3303-3312, 3337-40, 3355-6, 3468.

This list includes a wide range of common goods including for example:

- Organic compounds

- Gases

- Liquified petroleum gas

- Refrigerants

- Insecticides

- Fire extinguishers

Full details of UN numbers are widely published on the web.

It should be borne in mind that manufactured products containing one or more of these compounds (eg paints, tyres etc) can pose a similar hazard.

If there is any uncertainty about which items a vehicle will be used to transport then the precautionary principle should apply and appropriate ventilation should be fitted.